## Slide 1: BTP Mid-Term Report
Multi-Robot Task Orchestration for Construction Assembly
Project Overview

## Slide 2: Progress Till Now
Simulation Environment: Fully functional PyBullet setup
Robot Control & Kinematics: 7-DOF Panda arm, grasp-error compensation
Vision Integration: 3D CV pipeline for overhead camera detection
Task Orchestration & LLM Brain: Not started yet

## Slide 3: Quantified Current Progress
Vision Perception Accuracy (Overhead Camera):
  Mean 3D Pos Error: 3.96 mm | Mean Yaw Error: 0.18 degrees
Kinematic Placement Precision:
  Demonstrated robust grasp-error compensation during final placement.
  Typical Mean Placement Deviation: ~4.0 mm
System Reliability & Fault Recovery:
  First-try Pick Success Rate: 65%
  Ultimate Success Rate: 100% (Arm safely detects slip and recovers)

## Slide 4: Current Challenges
Workspace Constraints
Primary robotic arm operates in a fixed, static workspace
Limits maximum size and height of the wall
Transitioning to dynamic base placement or mobile base is complex

## Slide 5: Future Goals (Next 2 Months)
Refine LLM Orchestration: Transition to prompt-engineered LLM brain
Improve Physics Realism: Realistic kinematics and dynamic grasping
Comprehensive Benchmarking: Automated evaluations and Gantt charts
Final Project Deliverables: Documentation, defense, and code release